## Slide 1: Why is 802.11b 11 Mbps?
Stephen Lien
Technology Director
Redwood Area Schools
slien@redwoodareaschools.com
Understanding Wireless Data Transmissions, or…

## Slide 2: What’s this all about?
10Base-T: 10MHz x 1bpHz = 10Mbps
“OK Google, why is 802.11b 11Mbps?”
Not a wireless engineer
010011010
1Hz
1Hz
1Hz
1Hz
1Hz
1Hz
1Hz
1Hz

## Slide 3: Electromagnetic Fields
Remember this?
Field of electromagnetic force from the motion of an electric charge
Forms orthogonal to electron flow
Electron flow
Magnetic Field
Magnetic Field

## Slide 4: Radio Signals
+
–
–
+
I
I
Oscillating current in antenna = Radio Signal
Received signal induces current, reproduces sent signal

## Slide 5: Encoding Data Onto a Signal
Modulation: varying waveform properties
Three ways to modulate signal
  Amplitude
  Frequency
  Phase
802.11b Modulation

## Slide 6: Fixing Misconceptions
Frequency = data rate
Frequency is “carrier wave”
Data encoded onto carrier wave
Data rate < frequency
Max. data rate a function of signal strength and line noise

## Slide 7: Phase Shift Modulation
BPSK: binary phase shift keying
QPSK: quadrature phase shift keying
802.11b
Did it shift?
Did it shift?
Did it shift?
Did it shift?
Did it shift?
Did it shift?
Did it shift?
Did it shift?
How much?
How much?
How much?
0
1
0
1
00
01
11
10
dibit

## Slide 8: And Here Comes the Rabbit Hole!

## Slide 9: Handling Interference
1MHz Sub-Channel @ 2.442 GHz
NOISE
11MHz Channel

## Slide 10: Direct Sequence Spread Spectrum
1Mbps Recipe:
  To transmit one bit:
    0: transmit 0 0 1 1 0 0 1 1 0 1 1
    1: transmit 1 1 0 0 1 1 0 0 1 0 0
    Symbol rate = 1 million Symbols / sec.
    1MSps x 1 bit/S = 1Mbps
2Mbps Recipe:
  Transmit dibits
    1MSps x 2 bits/S = 2Mbps
11001100100
1
1
Symbol
Barker Codes

## Slide 11: DSSS, Continued
5.5Mbps Recipe:
  To transmit four bits:
    Symbol size shrunk from 11 to 8 dibits
    Symbols overlap on channels
    4 bits data encoded (CCK) onto 8 dibits
    (11 ÷ 8) MSps x 4 bit/S = 5.5Mbps
11Mbps Recipe:
  To transmit eight bits:
    8 bits encoded onto 8 dibits
    1.375 MSps x 8 bits/S = 11Mbps
0010
10111010
10101011
3/8
Next
Sym
0010

## Slide 12: For Reference’s Sake…
Consult your local 1700 page CWNA study guide
Or your 568 page Communications Engineering Desk Reference manual

## Slide 13: How Did Wi-Fi Get Faster?
Better modulation
  QPSK  64-QAM
    2 bit values  8 bit values
  Multiplexing (OFDM)
    Overlapping multiple signals on the same bandwidth
Multiple Antenna (MIMO)
Channel Bonding

## Slide 14: Where’s My Gigabit Wi-Fi?
Encoding reaching its limit
  Noise built into engineering
  More data = more loss
Higher frequencies?
  Signals don’t propagate
Channel Bonding on 5GHz
  9 20MHz Ch. @ 173Mbps
  4 40MHz Ch. @ 400Mbps
  2 80MHz Ch. @ 867Mbps

## Slide 15: To Fix the Problem…
E

## Slide 16: Wi-Fi 6e (802.11ax2 ?)
FCC opening 5.9GHz – 7.1Ghz spectrum
AKA “6GHz spectrum”
Existing frequencies?
14 80GHz 1Gbps channels
7 160GHz 2Gbps channels
Nothing formalized

## Slide 17: See Me w/ Questions
Very simplified information
Good to know what we’re dealing with
Please present @ Brainstorm!!!